## Slide 1: 网络测量算法研究
博士生开题报告
导一一师：尹 霞一教一授
研A究A生：赵宗义一一一一
2018年9月
Notes: 各位老师，大家好！我的名字叫赵宗义，现在是普博二年级在读，我的导师是尹霞老师，我开题的题目是“态势感知在校园网络中的应用研究”。

## Slide 2: 主要内容
一. 总体框架
二. 选题背景
三. 国内外研究现状
四. 研究内容及拟解决的主要问题
五. 研究方案及可行性分析
六. 可能的创新点及预期成果
七. 进度计划安排
八. 参考文献
文献
综述
选
题 报
告
Notes: 这是我的开题报告的主要内容。首先我会介绍一下我的研究框架和选题背景以及国内外研究现状，然后我会重点介绍我的研究方案，最后再陈述我的预期成果以及进度计划安排。
以下是我的研究框架

## Slide 3: 二. 选题背景（网络测量）
网络测量有两种方法：
sFlow代理对数据流进行采样
将采样得到的数据包发送到sFlow收集器
使用一定的数据结构记录经过的数据包的总结信息
需要时可以查询这个数据结构获取总结信息
Notes: 常用的网络测量有两种方法。一种是基于采样的方法，比如在sFlow中转发设备包含一个代理，这个代理会对经过的数据包进行采样，然后把采样得到的数据包转发到收集器中。
另一种方法是基于sketch的方法，这种方法在转发设备中维护一个数据结构，然后对经过的数据包记录总结信息，需要的时候我们可以查询这个数据结构获取总结信息

## Slide 4: 二. 选题背景（网络测量）
网络中在一个小时内可能会超过100万个流
则收集器中需要维护100万个数据项
每个数据项占内存100B，则收集器至少需要100MB的SRAM
路由器的带宽为10Gbps
假如完全记录每个数据包则最坏情况下每秒钟需要访问内存2亿次
假如只记录被采样的数据包，则不能正确估计小流
基于采样的测量方法存在严重的可扩展性问题
Notes: 骨干网中在一个小时内可能会超过100万个流经过一个路由器，所以收集器中需要维护100万个数据项。假设每个数据项占内存100B，则收集器至少需要100MB的SRAM。
假设路由器的带宽为10Gbps，假如完全记录每个数据包则最坏情况下每秒钟需要访问内存2亿次；而假如只记录被采样的数据包，则不能正确对小流进行估计。
所以基于采样的测量方法存在严重的可扩展性问题

## Slide 5: 二. 选题背景（网络测量）
基于sketch的测量方法需要消耗大量的计算资源，影响转发设备的速率
Notes: 而基于sketch的测量方法需要消耗大量的CPU资源，因而会严重影响转发设备的吞吐率，比如最近提出的几种测量方法，最差情况下处理每个数据包需要10454个时钟周期，而在10Gbps的网卡上只能达到5Gbps的吞率。

## Slide 6: 三. 国内外研究现状（网络测量）
SketchVisor [SIGCOMM’17]
UnivMon [SIGCOMM’16]
FlexSample [IMC’08]
S3 [IMC’06]
针对特定的流进行测量
针对大流进行测量
使用fast path来弥补sketch测量消耗CPU资源的不足
提供一个接口来满足不同测量的需求
Notes: 在网络测量方面，IMC 2006提出了一个针对大流的测量算法，但是有时候我们需要测量的可能是具有某些性质的流，所以IMC 2008提出的FlexSample允许我们指定需要测量的流
SIGCOMM 2016提出的UnivMon允许我们对不同的测量指标进行测量，而SIGCOMM 2017提出的SketchVisor使用了一个fast path，通过牺牲测量精度来解决基于sketch的方法消耗CPU资源较多的问题

## Slide 7: 三. 国内外研究现状（网络测量）
测量方案 | CPU消耗量 | 内存消耗量 | 测量对象 | 测量精度
SketchVisor | 小 | 小 | 所有流 | 低
UnivMon | 大 | 小 | 所有流 | 高
FlexSample | 小 | 小 | 部分流 | 高
S3 | 小 | 小 | 大流 | 高
基于采样的测量方法准确度不高
为提高测量精度只能对部分流进行测量
基于sketch的测量方法消耗CPU资源较多
为减少CPU资源消耗只能降低测量精度
Notes: 基于采样的方法测量精度不够，所以FlexSample和S3都采取了只对部分流进行测量的方法来提高测量精度，而基于sketch的方法需要消耗大量的CPU内存资源，因此要SketchVisor采用了降低测量精度的方法来减少CPU的资源消耗

## Slide 8: 五. 研究方案及可行性分析
设计分布式网络测量算法以减轻测量设备的计算负担
在网络边缘通过聚类算法进行botnet检测
通过硬件middlebox和NFV混合部署的方式降低middlebox的部署成本、提高NFV的性能
对无线路由器故障原因进行系统性研究，提高校园网网络稳定性
Notes: 首先是分布式网络测量算法的设计

## Slide 9: 五. 研究方案及可行性分析（A）
优点
只需要固定的内存
能够将测量误差控制在有限的范围之内
缺点
需要对每个数据包都进行大量的计算
需要消耗大量的CPU资源，影响转发设备的吞吐率
基于sketch的测量方案：
SDN网络：
SDN网络在数据中心网络和企业网中广泛部署
网络管理员对网络有完整的控制权
数据包在网络中的传输路径是可以预知的
Notes: 基于sketch的测量方案的优点是只需要固定的内存，而且能够将测量误差控制在有限的范围之内，因此得到了人们的青睐，但是它的一个严重的缺陷是它需要对每个数据包都进行大量的计算，因此会消耗大量的计算资源而影响转发设备的吞吐率。
SDN网络在数据中心网络和企业网中广泛部署，在SDN网络中网络管理员对网络有完整的控制权，而且数据包在网络中的传输路径是可以预知的

## Slide 10: 五. 研究方案及可行性分析（A）
预先计算数据流的转发路径
将测量任务分散在转发路径上不同的路由器中
路由器不用对每一个数据流进行测量
由收集器统一汇总各个设备的测量结果
分布式测量算法：
Notes: 所以我们的分布式测量算法会预先计算数据流的转发路径，然后将测量任务分配给转发路径上不同的路由器，每个路由器只需要对指定的流进行测量，最后由收集器统一汇总各个设备的测量结果

## Slide 11: 五. 研究方案及可行性分析（A）
传统数据中心网络中ToR交换机占75%，Core、AccR和AggS占15%
ToR-AggS、AggS-LB链路的利用率90%的情况低于24%，上层链路的利用率要高于下层链路
可以充分利用ToR交换机的计算能力进行网络测量
Notes: 有研究指出，在传统的数据中心中ToR交换机约占网络设备总数的75%，load balancer约占网络设备总数的10%，而ToR-AggS之间的链路、AggS-LB之间的链路的利用率在90%的情况下都要低于24%，所以我们可以把测量任务更多地分配在ToR交换机和Load Balancer等数量更多、负荷更小的设备上，这样便可以充分开发各种网络设备的潜力。

## Slide 12: 五. 研究方案及可行性分析（A）
缺陷：
只适用于集中控制的网络（SDN网络等）
挑战与困难：
设计映射方案保证每个流都能被映射到某台转发设备上
只能在一定程度上减轻转发设备的计算负担
设计查询算法，能够迅速地在上百个sketch结构上提取信息
Notes: 这种方法的缺陷是它只能适用于集中控制的网络，而且它减轻网络设备负担的能力是有限的，比如只能够将网络设备的负担减轻一个数量级。为了实现分布式测量方案，我们需要设计映射方案保证每个流都能被映射到某台转发设备上，同时我们不要设计查询算法，能够迅速地在上百个sketch结构上提取信息

## Slide 13: 六. 可能的创新点及预期成果
可能的创新点
设计一个分布式的网络测量算法
预期成果
对清华主页受到botnet攻击的问题提供解决方案
设计一个在网络边缘进行botnet检测的安全防御机制
设计一个NFV和middlebox的混合部署方案
设计一个无线路由器的自动故障检测和修复方案
对清华无线路由器的故障问题进行系统调研并给出相关意见
发表2-3篇CCF列表的B类及以上文章

## Slide 14: 七. 进度计划安排
完成NFV混合
部署方案的研究
文献阅读
及选题
完成botnet的检测
和防御方法研究
调研文献并设计
分布式测量算法
完成分布式
测量算法研究
调研文献并进行无线
路由器故障情况的测量
完成路由器自动故
障修复算法的研究
调研文献并设计
NFV混合部署方案
撰写论文
准备答辩
2018.4
2018.7
2018.10
2020.1
2019.10
2019.7
2019.1
2019.4
2020.3

## Slide 15: 主要内容
一. 总体框架
二. 选题背景
三. 国内外研究现状
四. 研究内容及拟解决的主要问题
五. 研究方案及可行性分析
六. 可能的创新点及预期成果
七. 进度计划安排
八. 参考文献
文献
综述
选
题 报
告

## Slide 16: 八. 参考文献
[1] Frederic Raspall, Sebastia Sallent and Josep Yufera, "Shared-State Sampling", in Proc. of ACM IMC, October 25–27, 2006, Rio de Janeiro, Brazil.
[2] Puneet Sharma, Zhichen Xu, Sujata Banerjee, and Sung-Ju Lee, "Estimating Network Proximity and Latency", ACM SIGCOMM Computer Communication Review, Volume 36, Number 3, July 2006.
[3] Lihua Yuan, Chen-Nee Chuah and Prasant Mohapatra, "ProgME: Towards Programmable Network MEasurement", in Proc. of ACM SIGCOMM, August 27–31, 2007, Kyoto, Japan.
[4] Yifei Yuan, Dong Lin, Ankit Mishra et al., "Quantitative Network Monitoring with NetQRE", in Proc. of ACM SIGCOMM, August 21-25, 2017, Los Angeles, CA, USA.
[5] Zaoxing Liu, Antonis Manousis, Gregory Vorsanger, et al., "One Sketch to Rule Them All: Rethinking Network Flow Monitoring with UnivMon", in Proc. of ACM SIGCOMM, August 22–26, 2016, Florianopolis, Brazil.
[6] Qun Huang, Xin Jin, Patrick P. C. Lee, et al., "SketchVisor: Robust Network Measurement for Software Packet Processing", in Proc. of ACM SIGCOMM, August 21−25, 2017, Los Angeles, CA, USA.
[7] Jeff Rasley, Brent Stephens, Colin Dixon, et al., "Planck: Millisecond-scale Monitoring and Control for Commodity Networks", in Proc. of ACM SIGCOMM, August 17–22, 2014, Chicago, IL, USA.
[8] P. Phaal, S. Panchen, N. McKee, "InMon Corporation’s sFlow: A Method for Monitoring Traffic in Switched and Routed Networks", Network Working Group, RFC 3176.
[9] Cristian Estan and George Varghese, "New Directions in Traffic Measurement and Accounting", in Proc. of ACM IMW, November l-2,2001. San Francisco, CA, USA.
[10] Minlan Yu, Lavanya Jose, Rui Miao, "Software Defined Traffic Measurement with OpenSketch", in Proc. of USENIX Association NSDI, April 02 - 05, 2013, Lombard, IL.

## Slide 17: 八. 参考文献（续）
[11] B. Claise, Ed., "Cisco Systems NetFlow Services Export Version 9", Network Working Group, RFC 3954.
[12] Srinivas Narayana, Anirudh Sivaraman, Vikram Nathan, et al., "Language-Directed Hardware Design for Network Performance Monitoring", in Proc. of ACM SIGCOMM, Los Angeles, CA, USA, August 21–25, 2017.
[13] Martin Andreoni Lopez, Renato Souza Silva, Igor D. Alvarenga, et al., "Collecting and Characterizing a Real Broadband Access Network Traffic Dataset", in Proc. of IEEE Cyber Security in Networking Conference (CSNet), October 18-20, 2017, Rio de Janeiro, Brazil.
[14] Liuying Sun, Anthony T.S. Ho, Zhe Xia, "Detection and Classification of Malicious Patterns In Network Traffic Using Benford’s Law", in Prec. of APSIPA Annual Summit and Conference, Malaysia, December 12-15, 2017.
[15] Anukool Lakhina, Mark Crovella, Christophe Diot, "Diagnosing Network-Wide Traffic Anomalies", in Prec. of ACM SIGCOMM, Aug. 30–Sept. 3, 2004, Portland, Oregon, USA.
[16] Phillipa Gill, Navendu Jain, Nachiappan Nagappan, "Understanding Network Failures in Data Centers: Measurement, Analysis, and Implications", in Prec. of ACM SIGCOMM, August 15-19, 2011, Toronto, Ontario, Canada.
[17] Kihong Park, Gitae Kim, Mark Crovellat, et al., "On the relationship between file sizes, transport protocols,and self-similar network traffic", in Prec. of IEEE ICNP, 29 Oct.-1 Nov., 1996, Columbus, OH, USA, USA.
[18] Guofei Gu, Roberto Perdisci, Junjie Zhang, et al., "BotMiner: Clustering Analysis of Network Traffic for Protocol- and Structure-Independent Botnet Detection", in Proc. of the 17th conference on Security symposium (SS), July 28 - August 01, 2008, San Jose, CA.

## Slide 18: 八. 参考文献（续）
[19] Guofei Gu, Junjie Zhang, and Wenke Lee, "BotSniffer: Detecting Botnet Command and Control Channels in Network Traffic",in Proc. of the Network and Distributed System Security Symposium (NDSS), USA, February 10th-13th 2008, San Diego, California.
[20] Claudia Pascoal, M. Rosario de Oliveira, Rui Valadas, et al., "Robust Feature Selection and Robust PCA for Internet Traffic Anomaly Detection", in Proc. of the IEEE INFOCOM, March 25-30, 2012, Orlando, FL, USA.
[21] Yu-Zhong Chen, Zi-Gang Huang, Shouhuai Xu, et al., "Spatiotemporal Patterns and Predictability of Cyberattacks", PLoS ONE 10(5): e0124472, doi:10.1371/journal.pone.0124472.
[22] Ignacio Cano, Srinivas Aiyar, Arvind Krishnamurthy, "Characterizing Private Clouds: A Large-Scale Empirical Analysis of Enterprise Clusters", in Proc. of ACM SoCC, October 05-07, 2016, Santa Clara, CA, USA.
[23] Theophilus Benson, Aditya Akella and David A. Maltz, "Network Traffic Characteristics of Data Centers in the Wild", in Proc. of IMC, November 1–3, 2010, Melbourne, Australia.
[24] Daniel Turner, Kirill Levchenko, Alex C. Snoeren, "California Fault Lines: Understanding the Causes and Impact of Network Failures", in Proc. of SIGCOMM, August 30–September 3, 2010, New Delhi, India.
[25] Ryosuke Miura, Yuuki Takano, Shinsuke Miwa, "GINTATE: Scalable and Extensible Deep Packet Inspection System for Encrypted Network Traffic", in Proc. of SoICT, December 7–8, 2017, Nha Trang City, Viet Nam.
[26] Pat Bosshart, Glen Gibb, Hun-Seok Kim, "Forwarding Metamorphosis: Fast Programmable Match-Action Processing in Hardware for SDN", in Proc. of SIGCOMM, August 12–16, 2013, Hong Kong, China.
[27] Sailesh Kumar, Jonathan Turner, John Williams, "Advanced Algorithms for Fast and Scalable Deep Packet Inspection", in Proc. of ACM ANCS, December 3-5, 2006, San Jose, California, USA.

## Slide 19: 八. 参考文献（续）
[28] Michela Becchi, Patrick Crowley, "An Improved Algorithm to Accelerate Regular Expression Evaluation", in Proc. of ACM ANCS, December 3–4, 2007, Orlando, Florida, USA.
[29] Sailesh Kumar, Sarang Dharmapurikar, Fang Yu, "Algorithms to Accelerate Multiple Regular Expressions Matching for Deep Packet Inspection", in Proc. of ACM SIGCOMM, September 11-15, 2006, Pisa, Italy.
[30] Pat Bosshart, Dan Daly, Glen Gibb, et al., "P4: Programming Protocol-Independent Packet Processors", ACM SIGCOMM Computer Communication Review, Volume 44, Number 3, July 2014.
[31] Martin Roesch, "Snort – Lightweight Intrusion Detection for Networks", in Proc. of LISA, Seattle, November 7–12, 1999, Washington, USA.
[32] Fang Yu, Zhifeng Chen, Yanlei Diao, "Fast and Memory-Efficient Regular Expression Matching for Deep Packet Inspection", in Proc. of ACM ANCS, December 3–5, 2006, San Jose, California, USA.
[33] Anirban Majumder, Rajeev Rastogi, Sriram Vanama, "Scalable Regular Expression Matching on Data Streams", in Proc. of ACM SIGMOD, June 9–12, 2008, Vancouver, BC, Canada.
[34] Randy Smith, Cristian Estan, Somesh Jha, et al., "Deflating the Big Bang: Fast and Scalable Deep Packet Inspection with Extended Finite Automata", in Proc. of ACM SIGCOMM, August 17–22, 2008, Seattle, Washington, USA.
[35] Vern Paxson, "Bro: a system for detecting network intruders in real-time", in Proc. of the 7th USENIX Security Symposium, January 26-29, 1998, San Antonio, TX, USA.
[36] Minlan Yu, Andreas Wundsam, Muruganantham Raju, "NOSIX: A Lightweight Portability Layer for the SDN OS", ACM SIGCOMM Computer Communication Review, Volume 44, Number 2, April 2014.
[37] Chen Sun, Jun Bi, Zhilong Zheng, et al., "NFP: Enabling Network Function Parallelism in NFV", in Proc. of ACM SIGCOMM, August 21–25, 2017, Los Angeles, CA, USA.

## Slide 20: 八. 参考文献（续）
[38] Aurojit Panda, Sangjin Han, Keon Jang, et al., "NetBricks: Taking the V out of NFV", in Proc. of USENIX Association OSDI, Savannah, GA, USA, November 2–4, 2016.
[39] Joao Martins, Mohamed Ahmed, Costin Raiciu, et al., "ClickOS and the Art of Network Function Virtualization", in Proc. of USENIX Association NSDI, Seattle, WA, USA, April 2–4, 2014.
[40] Aaron Gember-Jacobson, Raajay Viswanathan, Chaithan Prakash, et al., "OpenNF: Enabling Innovation in Network Function Control", in Proc. of ACM SIGCOMM, August 17–22, 2014, Chicago, IL, USA.
[41] Justine Sherry, Peter Xiang Gao, Soumya Basu, et al., "Rollback-Recovery for Middleboxes", in Proc. of ACM SIGCOMM, August 17 - 21, 2015, London, United Kingdom.
[42] Bojie Li, Kun Tan, Layong (Larry) Luo, "ClickNP: Highly Flexible and High Performance Network Processing with Reconfigurable Hardware", in Proc. of ACM SIGCOMM, August 22–26, 2016, Florianopolis, Brazil.
[43] Chang Lan, Justine Sherry, Raluca Ada Popa, et al., "Embark: Securely Outsourcing Middleboxes to the Cloud", in Proc. of NSDI, March 16-18, 2016, Santa Clara, CA, USA.
[44] Murad Kablan, Azzam Alsudais, Eric Keller, et al., "Stateless Network Functions: Breaking the Tight Coupling of State and Processing", in Proc. of NSDI, March 27-29, 2017, Boston, MA, USA.
[45] Muhammad Asim Jamshed, YoungGyoun Moon, Donghwi Kim, et al., "mOS: A Reusable Networking Stack for Flow Monitoring Middleboxes", in Proc. of NSDI, March 27-29, 2017, Boston, MA, USA.
[46] Junaid Khalid, Aaron Gember-Jacobson, Roney Michael, et al., "Paving the Way for NFV: Simplifying Middlebox Modifications Using StateAlyzr", in Proc. of NSDI, March 16-18, 2016, Santa Clara, CA, USA.

## Slide 21: 谢谢各位老师！

## Slide 22: HashFlow的架构
HashFlow的数据结构包括一个主表(M)和一个辅助表(A)
主表和辅助表中的桶的内容分别是(flowID, count)和(digest, count)的形式
个哈希函数，其中称为主表的深度
在主表中记录大流的详细信息，而在辅助表中记录小流的总结性信息

## Slide 23: HashFlow的算法描述
依次使用将数据包映射到主表中
如果在主表中找到合适的桶就对其进行更新，算法停止
否则用将数据包映射到辅助表中
满足条件时将辅助表中的数据流写回主表

## Slide 24: HashFlow的信息流

## Slide 25: HashFlow的优势
能够详细记录大流的信息
  适用于流量计费、流量工程等应用
能够记录小流的总结性信息
自动检测大流，当小流逐渐成长为大流时将小流从辅助表移回主表
对网络测量算法的影响较小

## Slide 26: HashFlow的性能优化
主表的组织形式：
  单一的大表
  个小表， ，其中，， 是第个小表的容量
假设主表容量为，需要插入个数据流
单一大表的空间利用率为，其中，
分层大表的空间利用率为
其中，